PI3EQX6741STZDE

Subject: PI3EQX6741STZDE ReDriver Application Evaluation Report

# From: Lingsan

# Date: 3/15/2011

Summary

- Phy Transmit Signal Requirement: TSG-01, TSG-02, TSG-03, TSG-04, OOB-02, OOB-03, OOB-04, OOB-05 are tested in Figure3 to Figure14.

- OOB signaling on/off time are checked in Figure15, PI3EQX6741ST can work with LSI card with normal OOB input/output in Figure16.

- Power consumption is measured in Table1 and one is in spec limitation of datasheet.

- Different eSATA HDD connection test are done and passed in Table2.

- Different internal HDD connection test are done and passed in Table3.

- PI3EQX6741ST can work for normal startup and reading/writing on Compal NB-PAL50 with Seagate HDD and other HDDs.

Part Information

Device Name: PI3EQX6741ST

Lots Number: N.A.

Part Marking: EQX6741STZDE JBHGC

Package: 20 pin TQFN (ZD)

Introduction

The report shows the performance of PI3EQX6741STZDE SATA3 ReDriver on evaluation board Rev.A. Figure1a&1b are top and bottom view of the board.

Figure1a. Top view of PI3EQX6741STZDE Eval Board Rev.A

Figure1b. Bottom view of PI3EQX6741STZDE Eval Board Rev.A

Test Setup

There is test point on the board, TP1 for A_OUT and TP2 for B_OUT differential pair in Figure2

Control Signal Setting:

TDet_EN=LOW,

A_EM&B_EM=LOW

A_EQ&B_EQ=LOW

Test Equipment:

Agilent Infiniium 54855A Digital Sampling Oscilloscope

Agilent E2695A probe Head

Agilent E2677A probe Head

SATA test fixture

AMD mother board

Intel mother board

SIIG 6G SATA Card

External Hard Disk

Udisk with DOS system

SATA cable

Ru software for AMD BIOS setting

Figure2. Test Point Setting

Test Items and Result

- Unit Interval

Figure3 shows unit interval of Gen1 (1.5G) and Gen2 (3.0G). Test point is TP1.

| UI for Gen1 (665.83) | UI for Gen2 (332.6ps) |
| --- | --- |

Figure3. UI for Gen1 and Gen2

- TSG-01 Differential Output Voltage

Figure4 shows differential output voltage of Gen1 (1.5G) and Gen2 (3.0G). Test point is TP1.

| Gen1 (642.82mV) | Gen2 (630.72mV) |
| --- | --- |

Figure4. Differential Output Voltage for Gen1 and Gen2

- TSG-02 Rise/Fall Time

Figure5 and Figure6 show rise time and fall time of Gen1 (1.5G) and Gen2 (3.0G). Test point is TP1.

| Rise Time for Gen1 (89.3ps) | Fall Time for Gen1 (90.6ps) |
| --- | --- |

Figure5. Rise Time and Fall Time for Gen1

| Rise Time for Gen2 (87.8ps) | Fall Time for Gen2 (89.4ps) |
| --- | --- |

Figure6. Rise Time and Fall Time for Gen2

- TSG-03 Differential Skew

Figure7 shows differential skew of Gen1 (1.5G) and Gen2 (3.0G). Test point is TP1.

| Gen1 (9.45ps) | Gen2 (7.64ps) |
| --- | --- |

Figure7. Differential Skew for Gen1 and Gen2

- TSG-04 AC Common Mode Voltage

Figure8 shows differential skew of Gen1 (1.5G) and Gen2 (3.0G). Test point is TP1.

| Gen1 (32.6/2=16.3mV) | Gen2 (31.6/2=15.8mV) |
| --- | --- |

Figure8. AC Common Mode Voltage for Gen1 and Gen2

- OOB Signaling Process

Figure9 shows OOB signaling process. Test point is TP1&TP2.

OOB Signaling Process

Figure9 OOB Signaling Process

- OOB-01 UI during OOB Signaling

Figure10 shows UI during OOB signaling. Test point is TP1.

UI during OOB Signaling( 654.5ps)

Figure10 UI during OOB Signaling

- OOB-03 COMINIT/RESET Transmit Burst Length

Figure11 shows COMINIT/RESET Transmit Burst Length. Test point is TP1.

Burst Length(107.6ns)

Figure11. COMINIT/RESET Transmit Burst Length

- OOB-04 COMINIT/RESET Transmit Burst Gap Length

Figure12 shows COMINIT/RESET Transmit Burst Gap. Test point is TP1.

Burst Gap Length(318.8ns)

Figure12. COMINIT/RESET Transmit Burst Gap Length

- OOB-05 COMWAKE Transmit Burst Length

Figure13 shows COMWAKE Transmit Burst Length. Test point is TP1.

Burst Length(108.1ns)

Figure13. COMWAKE Transmit Burst Length

- OOB-03 COMWAKE Transmit Burst Gap Length

Figure14 shows COMWAKE Transmit Burst Gap. Test point is TP1.

Burst Gap Length(105.4ns)

Figure14. COMWAKE Transmit Burst Gap Length

- OOB on/off Time

Figure15. 1st OOB Burst Length.

| 1st OOB Burst |
| --- |
| OOB on time(8.86ns) | OOB off time(6.82ns) |

Figure15. OOB on/off time

- Initial OOB Process with LSI SAS Card

Figure16.  Initial OOB Process with LSI SAS card

| Initial OOB Process | 4th Section of OOB |
| --- | --- |

Figure16. Initial OOB Process with LSI SAS card

Power Consumption Test

Below table is power consumption test result for PI3EQX6741ST at 6Gb/s.

Table1. Power consumption Test Result with PI3EQX6741STZDE

| Test Condition | Voltage (Unit: V) | Current (Unit: mA) | Power Consumption (Unit: mW) |
| --- | --- | --- | --- |
| Active (no Pre-em of CH A&B) | 3.30 | 77.20 | 254.76 |
| Active (w/ Pre-emphasis of CH A) | 3.30 | 86.30 | 284.79 |
| Active (w/ Pre-emphasis of CH B) | 3.30 | 86.40 | 285.12 |
| Active (w/ Pre-emphasis of CH A&B) | 3.30 | 95.60 | 315.48 |
| HDD Unplugged (w/o HDD,Tdet_EN=High) | 3.30 | 1.03 | 3.40 |
| Slumber mode (w/o HDD or Host,Tdet_EN=low) | 3.30 | 11.30 | 37.29 |
| Standby Mode (EN=Low) | 3.30 | 0.02 | 0.07 |

Different eSATA HDD Connection Test

Figure17 shows the connection setup and Table2 is different eSATA HDD connection test result.

Figure17. Different eHDD connection Test Setup

Table2. Different eSATA HDD connection Test Result with PI3EQX6741STZDE

| Lab S/N | Model Name or P/N | Manufacturer | w/ Bridge IC | Test Results |
| --- | --- | --- | --- | --- |
|  |  |  | IC Name | Vendor | D.C. |  |
| BD-001 | T12s/su | JJERA TECHNOLOGY | SPIF225A-HL231 | SunPlusIT | 0805 | pass |
| BD-002 | YX-32 | PHIYO | JM20316 | JMicron | 0635 | pass |
| BD-003 | BXE-20A | Zynet | INIC-1610L | Initio | 0711 | pass |
| BD-004 | T12su | JJERA TECHNOLOGY | INIC-1610PL | Initio | 1004 | pass |
| BD-005 | HD3-S2 | Mediasonic | SPIF225A-HL231 | SunPlusIT | 0626 | pass |
| BD-006 | SSK | SzBroad Technology | JM20336 | JMicron | 1010 | pass |
| BD-007 | 9NL6AG-500 | Seagate | OXU931DS | Oxford Semi | 0648 | pass |

Different Internal SATA HDD Connection Test

Figure18 shows the connection using MB and Table3 is different internal SATA HDD result.

Figure18. Different Internal SATA HDD connection Test Setup with MB and PI3EQX6741STZDE

Table3. Different internal SATA HDD  using MB with PI3EQX6741STZDE

| Lab S/N | Motherboard/Card | Vendor | Chipset or IC Vendor | Test Result |
| --- | --- | --- | --- | --- |
| MB-001 | GA-EG45M-UD2H | GigaByte | Intel | pass |
| MB-002 | A780Full | ASRock | AMD | pass |
| AD-001 | SATA 6Gb/s Adapter | SIIG | Marvell | pass |
| AD-002 | SAS 8704ELP | LSI | LSI | pass |

History

Version 1.0	Original Version	Mar 15, 2011

# Text boxes

MB

TP2

TP1

EQX6701CZDE

PI3EQX6741ST EVB