PI3PCIE3413/PI2EQX59xx/PI3EQX58xx/PI2EQX88xx

PCIE switch/re-driver debug App Note

By YT Tso and Jessy Chen

- Introduce:

Use simple way to check PCIE function is work or not.

For PI3PCIE3413, PI2EQX59xx, PI3EQX58xx, PI2EQX88xx  debug purpose.

Figure 1 top view of PI3PCIE3413 EVB

- Check PCIE function workable: RX.detect

Please check the PCIE function as below block diagram

Step1. Remove red one block as below

Step2. Measurement the place at TP1

TP1 Test result

- Check PCIE function workable: With AC cap / Without AC cap different

Please check the PCIE function as below block diagram after power on

Step1. Test TP2

Step2. Test TP3

TP2

TP2 Test result

TP3 Test result

- Check PCIE function workable: From Rx.detect (polling(L0

Please check the PCIE function as below block diagram after power on

Step1. Test TP2 when power on

TP2 Test result

- Check PCIE re-driver link status: Throw h/w or s/w register

Please check the PCIE function as below block diagram after power on

# Text boxes

Zoom in

TP1: Detect Pulse

Detect Pulse

Detect Pulse Zoom In

TP1: Detect Pulse Zoom In

~160us

~505mV

TP2: Before AC cap

PCIe Gen2 : 5Gbps

DC BIAS

TP3: After AC cap

PCIe Gen2 : 5Gbps

Vcm = 0V

Gen1 Speed:

2.5Gbps

TP2: Before AC

L0: Gen2 5.0Gbps

RX.detect

Polling

Power on