PI3EQX7742(I)

PI3EQX7742(I) EVB Rev.A User Manual

By YT Tso, Anne Wu and Jessy Chen

- Introduce:

PI3EQX7742(I) is a 2-port, low power, high performance 5.0Gbps signal ReDriver designed for USB3.0 protocol. The device provides programmable Equalization (EQ), De-Emphasis (DE) and input threshold controls to optimize performance over a variety of physical mediums by reducing Inter-Symbol Interference (ISI)

- Quick Start — For Default Setting:

To start-up the PI3EQX7742(I) EVB, complete the following steps:

- Check the head pin status and follow Table 1 & Table 2.

- Connect the JP1/JP3 on EVB to PC’s USB3.0 port through a USB3.0 Type A to B cable.

- Plug the USB3.0 device into EVB USB Type-A connector JP2/JP4 through USB3.0 cable

Figure.1 Top view of PI3EQX7742(I) EVB & pin-strap defaulted setting

Table 1--Header pin is set as defaulted on EVB.

| Header pin # | Pin name for PI3EQX7742(I) | Switch status | Remark |
| --- | --- | --- | --- |
| JP5 | VDD | Short | Power on PI3EQX7742(I) both ports |
| JP6 | EN_A# | Open | Channel A on Normal Operating Mode |
| JP7 | EN_B# | Open | Channel B on Normal Operating Mode |
| JP8 | EN_C# | Open | Channel C on Normal Operating Mode |
| JP9 | EN_D# | Open | Channel D on Normal Operating Mode |
| JP10 | RXDET_AB | Open | Channel A&B receiver detection are active |
| JP12 | RXDET_CD | Open | Channel C&D receiver detection are active |
| JP13 | VTH_AB | Open | Channel A&B VTH=HIGH=100mVppd |
| JP15 | VTH_CD | Open | Channel C&D VTH=HIGH=100mVppd |

Figure.2 Top view of PI3EQX7742(I) EVB on SW1/SW2 defaulted setting

Table 2—SW1/SW2 set as defaulted on EVB.

| SW1-1 SW1-2 | DE_D | SW1-1 = ON SW1-2 = OFF | Channel D de-emphasis setting= 0dB (low) |
| --- | --- | --- | --- |
| SW1-3 SW1-4 | EQ_D | SW1-3 = ON SW1-4 = OFF | Channel D Equalizer setting= 3dB (low) |
| SW1-5 SW1-6 | DE_C | SW1-5 = ON SW1-6 = OFF | Channel C de-emphasis setting= 0dB (low) |
| SW1-7 SW1-8 | EQ_C | SW1-7 = ON SW1-8 = OFF | Channel C Equalizer setting= 3dB (low) |
| SW2-1 SW2-2 | DE_B | SW2-1 = ON SW2-2 = OFF | Channel B de-emphasis setting= 0dB (low) |
| SW2-3 SW2-4 | EQ_B | SW2-3 = ON SW1-4 = OFF | Channel B Equalizer setting= 3dB (low) |
| SW2-5 SW2-6 | DE_A | SW1-5 = ON SW1-6 = OFF | Channel A de-emphasis setting= 0dB (low) |
| SW2-7 SW2-8 | EQ_A | SW1-7 = ON SW1-8 = OFF | Channel A Equalizer setting= 3dB (low) |

Equalizer setting:

| Header pin # | Pin name for PI3EQX7742(I) | Switch status | Remark |
| --- | --- | --- | --- |
| SW1-3 SW1-4 | EQ_B | SW1-3 = ON SW1-4 = OFF |  |
| SW1-7 SW1-8 | EQ_A | SW1-7 = ON SW1-8 = OFF |  |
| SW2-3 SW2-4 | EQ_D | SW2-3 = ON SW1-4 = OFF |  |
| SW2-7 SW2-8 | EQ_C | SW1-7 = ON SW1-8 = OFF |  |

De- emphasis setting:

| Header pin # | Pin name for PI3EQX7742(I) | Switch status | Remark |
| --- | --- | --- | --- |
| SW1-1 SW1-2 | DE_B | SW1-1 = ON SW1-2 = OFF |  |
| SW1-5 SW1-6 | DE_A | SW1-5 = ON SW1-6 = OFF |  |
| SW2-1 SW2-2 | DE_D | SW2-1 = ON SW2-2 = OFF |  |
| SW2-5 SW2-6 | DE_C | SW1-5 = ON SW1-6 = OFF |  |

VTH setting:

| Header pin # | Pin name for PI3EQX7742(I) | Switch status | Remark |
| --- | --- | --- | --- |
| JP13 | VTH_AB | Open |  |
| JP15 | VTH_CD | Open |  |

PI3EQX7742(I) EVB Schematic

PI3EQX7742(I) PCB Layout

Figure.2 Top view of PI3EQX7742(I) EVB Layout

Figure.3 Bottom view of PI3EQX7742(I) EVB Layout

# Text boxes

DE_C=0dB

JP2

EQ_C=3dB

D channel, 2nd port

EQ_D=3dB

DE_D=0dB

JP4

C channel, 2nd port

JP1

JP3

SW1: 2nd port

SW1-1=ON

SW1-2=OFF

SW1-3=ON

SW1-4=OFF

SW1-5=ON

SW1-6=OFF

SW1-7=ON

SW1-8=OFF

B channel, 1st port

JP5 Short to VDD=Power on IC

RXDET_AB (JP10)/CD (JP12)

= Open

= Channel AB/CD->Receiver Active

DE_A=0dB

EQ_A=3dB

EQ_B=3dB

DE_B=0dB

EN_A# (JP6)/B#(JP7)/C#(JP8)/D#(JP9)

= Open

= Channel A/B/C/D-> Normal Mode

VTH_CD (JP15)/AB (JP13)

= Open

= Channel AB/CD ->100mVppd

A channel, 1st port

SW2: 1st port

SW2-1=ON

SW2-2=OFF

SW2-3=ON

SW2-4=OFF

SW2-5=ON

SW2-6=OFF

SW2-7=ON

SW2-8=OFF