PI3HDMI101-B Demo Board Rev.B User Manual 
by Ada Yip

Table of Contents

- Introduction

- Overview

- Quick Start

- Key Circuit Description

- Demo Board Schematic

- BOM List

1.0 Introduction

To support long trace or cable in HDMI application, HDMI re-driver is an essential device.  This user manual describes the components and the usage of PI3HDMI101-B implemented on PI3HDMI101 Demo Board Rev.B. Rx-sense feature offered in PI3HDMI101 has been designed in each TMDS of PI3HDMI101-B. Thus, PI3HDMI101-B detects the presence of receiver automatically.

2.0 Overview

Figures 1 and 2 are the top view and bottom view of PI3HDMI101 demo board.

Figure 1: Top View of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

Figure 2: Bottom View of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

3.0 Quick Start

To quick start PI3HDMI101-B on PI3HDMI101 demo board, complete the following steps:

- Keep all pins of DIP-8 switch at reference SW101 not shorted to GND; in this case, Swing = 500mV, Pre-emphasis = 0dB, Equalization = Optimized EQ, and IADJ = high

- Short pins 2 and 3 of 3-pin header at reference J103 together to enable DDC channel

- Short pins 1 and 2 of 3-pin header at reference J104 together to enable TMDS output

- Short 2-pin header at reference JP102 so that the 5V from source can be used for powering up PI3HDMI101 demo board

- Short 2-pin header at reference JP103 so that 5V from source can be employed to sink device

- Employ a 5V from mini-USB connector at reference J106

- Connect HDMI source, e.g. DVD player, to HDMI connector at reference J101

- Connect HDMI output connector at reference J102 to an HDMI sink device, e.g. HDTV

4.0 Key Circuit Description

4.1 Power Circuit

5V of PI3HDMI101 demo board can be supplied via three ways, i.e. using 5V supplied from Input Port, Power Jack, or from USB Type B Connector. Jumpers on demo boards are not connected at default. If using voltage of input port to power up the entire board, jumper must be added at JP102. JP103 is shorted so as to supply 5V to +5V pin at the output HDMI connector J102.

Figure 3: Schematic of 5V Power Supply of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

4.2 HPD Circuitry

Assuming that a Source is connected to HDMI connector J101, after a Sink is attached to HDMI connector J102, Sink will signal the source it is connected by pulling HPD_C1 signal (HPD pin of J102) to high level. HPD_A1 signal (HPD pin of J101) will be pulled up by +5V supplied by Source in the circuit shown below.

Figure 4: Schematic of Sink HPD of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

4.3 HPD Circuitry

One AT24C02B EEPROM is implemented in PI3HDMI101 demo board to model I2C application. The EEPROM is for DDC line capacitance measurement purpose. Please refer to p.16 for measurement result. A0 and A1 address inputs of AT24C02B are pulled to low by external pull-down resistors while address A2 is pulled high. Write protection of the EEPROM is disabled.

Figure 5: Schematic of EEPROM of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

4.4 IADJ Feature

Voltage selection using IADJ pin 42 for I2C buffer of PI3HDMI101 is chosen according to I2C external pull-up range at output connector J102. IADJ is set to high via a resistor R104 at default in the schematic above. Switch SW101 is used to change IADJ to low. IADJ should be set to high if external pull-up at output connector ranges from 1kΩ to 2kΩ or low if external pull-up is larger than 3kΩ. 2kΩ pull-ups are employed at R107 and 108 on PI3HDMI101 HDMI-HDMI demo board as shown below.

Figure 6: External DDC Pull-up of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

4.5 Fail-safe Feature

When source chipset does not generate CLK signal, noise may pass through an active PI3HDMI101 to cause output oscillation. To implement fail-safe feature to prevent from output oscillation, the input CLK is recommended to be biased externally. 100mV DC bias can be added to CLK+ by adding a 1.5kΩ pull-down resistor. To maintain trace impedance consistency, it is recommended to avoid stub between pull-down resistor pad and CLK signal trace on PCB layout.

Figure 7: External Pull-down Resistors at Input CLK of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

In some DVD players, no sink current circuitry is implemented in TMDS. When these DVD players are de-selected, CLK signals stay at high level. To ensure the DVD players can enter idle mode when being de-selected, input CLK+/- pins are pulled down externally. By keeping 1.5kΩ pull-down resistor at CLK+ unchanged, another 22kΩ resistor is added to CLK- to pull CLK to low level when there is no 50Ω termination. HDCP can then be reset by RxSense when the port is being selected back.

4.6 Rx-Sense

As Rx-Sense detection circuit is implemented in PI3HDMI101-B, the original Rx-Sense pin (pin 16) of PI3HDMI101 is now designed as VDD. Thus, pin 16 should be always tied to high level via 47kΩ resistor at reference R105 on demo board. Pin 13 of DIP-8 switch at reference SW101 should not be shorted to GND at any time.

Figure 8: Rx-Sense of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

5.0 Demo Board Schematic

Figure 9: Schematic of PI3HDMI101 HDMI-HDMI Demo Board Rev.B

6.0 BOM List

| Item | Quantity | Reference | Description |
| --- | --- | --- | --- |
| 1 | 8 | C101, C102, C103, C104, C105, C106, C107, C108 | 0.1uF Capacitor |
| 2 | 1 | C109 | 22uF Capacitor |
| 3 | 2 | C110, C111 | 1uF Capacitor |
| 4 | 3 | D101, D102, D103 | B0520LW Schottky Rectifier |
| 5 | 3 | JP101, JP102, JP103 | 2-pin Header |
| 6 | 2 | J101, J102 | HDMI Receptacle Connector |
| 7 | 2 | J103, J104 | 3-pin Header |
| 8 | 1 | J105 | Power Jack |
| 9 | 1 | J106 | Mini USB Type B Connector |
| 10 | 1 | Q101 | MMBT3906 PNP Transistor |
| 11 | 1 | Q102 | MMBT3904 NPN Transistor |
| 12 | 5 | R109, R110, R112, R115, R117 | NOT AVAILABLE |
| 13 | 9 | R101, R102, R103, R104, R105, R111, R113, R114, R116 | 47kΩ Resistor |
| 14 | 2 | R108, R119 | 10kΩ Resistor |
| 15 | 2 | R106, R107 | 2kΩ Resistor |
| 16 | 1 | R118 | 0Ω Resistor |
| 17 | 2 | R120, R122 | 20kΩ Resistor |
| 18 | 1 | R121 | 100kΩ Resistor |
| 19 | 1 | R123 | 1.5kΩ Resistor |
| 20 | 1 | R124 | 22 kΩ Resistor |
| 21 | 1 | SW101 | DIP-8 Switch |
| 22 | 1 | U101 | PI3HDMI101 HDMI Switch |
| 23 | 1 | U102 | AT24C02B EEPROM |
| 24 | 1 | U103 | 1117 Regulator |

Table 1: BOM List of PI3HDMI101 HDMI-HDMI Demo Board Rev.B