PI3HDMI301

2-Layer Demo Board Rev.A User Manual

by Ada Yip

Introduction

This user manual describes the components and the usage of PI3HDMI301 2-Layer HDMI-HDMI Demo Board Rev.A. To be more cost effective, 2-layer instead of 4-layer PCB is designed. As ground layer is not present in 2-layer PCB, reference ground has to be ensured continuous. Closer view of layout next to PI3HDMI301 is attached in Appendix C.

- Overview

- Quick Start

- Detailed Description

- Test Result

Overview

Figure 1 is the block diagram of Pericom PI3HDMI301 2-Layer Demo Board and Figures 2a and b show the top and bottom views of the demo board. There are three HDMI Type A receptacle connectors (J301-3), which are used to connect to HDMI source devices, such as DVD players. The HDMI Type A plug connector (J304) is used to connect to an HDMI sink device, such as HDTV. The demo board can be powered up by +5V DC from mini USB female connector (J306) or by delivering the 5V power of source to 3.3V regulator (U302). Swing, pre-emphasis and equalization of PI3HDMI301 can be adjusted using an 8-pin switch (SW301). A DP3T switch (SW302) is used to select HDMI port among ports 1, 2 and 3. The EEPROMs, which are used to model the DDC capacitance of EEPROMs in sink device, are optional and are not assembled on the demo board.

Figure 1: Block Diagram of PI3HDMI301 2-Layer Demo Board

Figure 2a: Top View of PI3HDMI301 2-Layer Demo Board

Figure 2b: Bottom View of PI3HDMI301 2-Layer Demo Board

Quick Start

To start-up the PI3HDMI301 2-Layer Demo Board, complete the following steps:

- Short /OE pin to GND using second last pin of SW301 8-pin switch in order to enable PI3HDMI301;

- Set Swing and Pre-emphasis to 500mV and 0dB, respectively, using pins 3-6 of SW301 switch;

- Set optimum EQ settings using pins 1-2 of SW301 switch regarding to Table 1;

- Place jumper at JP301 to provide 5V to Sink;

- Supply 5V to demo board from USB Connector at J306 or get the 5V power from Source by shorting JP302;

- Connect Sources, e.g. DVD players, to HDMI Input Connectors at J301, 302 and/or 303;

- Connect Sink, e.g. HDTV, to HDMI Output Connector at J304;

- Select desired HDMI port using SW302 DP3T switch.

Figure 3: Layout of PI3HDMI301 2-Layer Demo Board (Top View)

| Equalization | Input Trace |
| --- | --- |
| 3 dB | 4 – 8” |
| 8 dB | 8 – 16” |
| 12 dB (Optimized) | 12 – 18” |
| 15 dB | 16 – 24” |

Table 1: Optimized EQ Setting in Sink Application

Detailed Description

- An HPD pulse of 250ms is generated at HPD_D3_1 pin when switching port via switch SW302 in the following circuit. This pulse is sent back to HPD_SINK pin of PI3HDMI301 to introduce an HPD reset signal.

Figure 4: HPD Reset Pulse Circuit

The pulse will be delivered to the HPD pin of one selected port among three, HPD_A3_1, HPD_B3_1 or HPD_C3_1. This pulse will then initiate a reset of HPD at input connector side, HPD_A3, HPD_B3 or HPD_C3, through NPN transistor, Q304, Q305 or Q306, respectively. The reset circuit of port 1 is shown below. Resetting HPD is to ensure that HDCP Transmitter Link State is reset back to reset state H0. For details, please refer to Application Note AN202.

Figure 5: Source HPD Reset

- If Sink receiver is not connected to HDMI connector J304, HPD_D3 pin will become low. As shown in the above figure, the low HPD_D3 will turn on PNP transistor Q303 and then three NPN transistors Q304, Q305 and Q306. As a result, all the HPD signals at source side are pulled low and reset to state H0.

- When source chipset does not generate CLK signal, noise may pass through an active PI3HDMI301 to cause output oscillation. To implement fail-safe feature to prevent from output oscillation, the input CLK is recommended to be biased externally. 100mV DC bias can be added to CLK+ by adding a 1.5kΩ pull-down resistor. To maintain trace impedance consistency, it is recommended to avoid stub between pull-down resistor pad and CLK signal trace on PCB layout.

Figure 6: Input CLK External Pull-down

In some DVD players, no sink current circuitry is implemented in TMDS. When these DVD players are de-selected, CLK signals stay at high level. To ensure the DVD players can enter idle mode when being de-selected, input CLK+/- pins are pulled down externally. By keeping 1.5kΩ pull-down resistor at CLK+ unchanged, another 22kΩ resistor is added to CLK- to pull CLK to low level when there is no 50Ω termination. HDCP can then be reset by RxSense.

Test Result

- The eye diagram test in Test ID 7-10 of CTS is performed to determine the optimized EQ setting when 10m 28AWG HDMI cable is connected to J302, the input HDMI connector with 4” trace. A 1080p/60Hz, 8-bit Standard Color, Acer1 test pattern from Quantum Data is used as source. 500mV swing and 0dB pre-emphasis are chosen during the test. Output eye diagrams with different equalization settings are captured at TMDS D0 at HDMI output port (J304) of PI3HDMI301 2-Layer Demo Board.

Figure 7: Eye Diagram of 3dB EQ with 10m Cable at Port 2

Figure 8: Eye Diagram of 8dB EQ with 10m Cable at Port 2

Figure 9: Eye Diagram of 12dB EQ with 10m Cable at Port 2

Figure 10: Eye Diagram of 15dB EQ with 10m Cable at Port 2

On top of HDMI source eye diagrams shown above, the data jitter values are documented to show that a passing source eye with 10m cable at input port 2 can be obtained for any equalization setting greater than 8dB. The source eye mask is just for reference for Sink Application.

| Data Jitter |
| --- |
| 3dB EQ | 8dB EQ | 12dB EQ | 15dB EQ |
| 0.350 TBIT | 0.255 TBIT | 0.226 TBIT | 0.171 TBIT |

Table 2: Data Jitters with Different EQ Settings

- Termination Voltage in Test ID 8-4 is performed at J302 input HDMI connector.

| Output | Vterm | Spec | Units |
| --- | --- | --- | --- |
|  |  | Min | Max |  |
| D2+ | 3.29 | 3.125 | 3.475 | V |
| D2- | 3.29 | 3.125 | 3.475 | V |
| D1+ | 3.29 | 3.125 | 3.475 | V |
| D1- | 3.29 | 3.125 | 3.475 | V |
| D0+ | 3.29 | 3.125 | 3.475 | V |
| D0- | 3.29 | 3.125 | 3.475 | V |
| CLK+ | 3.18 | 3.125 | 3.475 | V |
| CLK- | 3.28 | 3.125 | 3.475 | V |

Table 3: Termination Voltage Result at J302

- Jitter Tolerance in Test ID 8-7 is performed when Data Generator is connected to J302 input HDMI connector and J304 output HDMI connector is attached to Philips 1080p HDTV.

Based on HDMI CTS 1.3c, 0.25*TBIT C_JITTER and 0.3*TBIT D_JITTER are set at Test Points TP1 (or 0.3*TBIT C_JITTER and 0.5*TBIT D_JITTER are set at Test Points TP2). Test setup below shows the locations of TP1 and TP2. Jitter Tolerance Test is performed when TMDS_CLOCK to TMDS_DATA skew is set to 0.0TBIT to 1.0TBIT with 0.1TBIT step.

Figure 11: Jitter Tolerance Test Setup

Jitter Tolerance Test is performed at HDMI Connector J302 of PI3HDMI301 2-layer demo board at 1920x1080p, 60Hz refresh rate and 8-bit color rate.

| C_JITTER (TBIT) at TP1 | C_JITTER Freq. (MHz) | D_JITTER (TBIT) at TP2 | D_JITTER Freq. (MHz) | Jitter Tolerance with CLK-DATA Skew = 0.0 to 1.0TBIT |
| --- | --- | --- | --- | --- |
| 0.25 | 10.0 | 0.50 | 0.5 | Pass @0.0 to 1.0TBIT Skew |
| 0.30 | 10.0 | 0.60 | 0.5 | Pass @0.0 to 1.0TBIT Skew |
| 0.25 | 7.0 | 0.50 | 1.0 | Pass @0.0 to 1.0TBIT Skew |
| 0.30 | 7.0 | 0.60 | 1.0 | Pass @0.0 to 1.0TBIT Skew |

Table 4: Jitter Tolerance Result at J302

- TMDS Differential Impedance in Test ID 8-8 at each port is checked.

| Port | Through Impedance | D2 | D1 | D0 | CLK | Spec | Units |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Min | Max |  |
| J301 | Min | 86 | 87 | 87 | 91 | 85 | 115 | ( |
|  | Max | 108 | 104 | 105 | 104 | 85 | 115 | ( |
| J302 | Min | 89 | 89 | 89 | 91 | 85 | 115 | ( |
|  | Max | 107 | 104 | 105 | 104 | 85 | 115 | ( |
| J303 | Min | 86 | 86 | 86 | 90 | 85 | 115 | ( |
|  | Max | 106 | 103 | 105 | 104 | 85 | 115 | ( |

Table 5: TDR Result

- HPD Output Voltage and Resistance in Test IDs 8-10 and 11 are tested at J302 input HDMI connector.

| Parameter | DUT Power | P_5V | VHPD | Spec | Units |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Min | Max |  |
| VHPD_L | Off | 0.0V | 0.00 | 0.0 | 0.4 | V |
|  | Standby | 0.0V | 0.00 | 0.0 | 0.4 |  |
|  | On | 0.0V | 0.00 | 0.0 | 0.4 | V |
| VHPD_H | On | 4.8V | 4.79 | 2.4 | 5.3 | V |
|  | On | 5.3V | 5.29 | 2.4 | 5.3 | V |

Table 6: HPD Output Voltage Result at J302

| Parameter | J302 | Spec | Units |
| --- | --- | --- | --- |
|  |  | Min | Max |  |
| VA | 4.99 | NA | NA | V |
| VB | 4.55 | NA | NA | V |
| ZHPD | 967 | 800 | 1200 | Ω |

ZHPD = (VA/VB – 1) * 10,000

Table 7: HPD Output Resistance Result at J302

Appendix A: Test Equipments

- Agilent Power Supply

- Agilent 54855A DSO with 1134A 7GHz Probe System and E2675A Differential Solder-in Probe Heads

- TDS8000 Digital Sampling Oscilloscope

- Tektronix DTG5334 Data Timing Generator with DTG30 and DTG32 Modules

- Agilent 33120A Function Generator

- R&S SMY02 Signal Generator

- Philips 37PFL7422 1080p HDTV

- Pericom 48” Trace Cards (Modeling Cable Emulator)

- 36” SMA-SMA Cables

- Pericom SMA-to-HDMI Test Fixture

- Multimeter

Appendix B: PI3HDMI301 2-layer Demo Board Schematic

For clearer view of schematic diagram, please click the PDF file icon on the right.

Appendix C: PCB Layout

Top View

Bottom View

Appendix D: BOM List

| Item | Quantity | Reference | Description |
| --- | --- | --- | --- |
| 1 | 13 | C301, C302, C303, C304, C305, C306, C307, C308, C309, C310, C317, C318, C319 | 0.1uF Capacitor |
| 2 | 1 | C314 | 22uF Capacitor |
| 3 | 2 | C315, C316 | 1uF Capacitor |
| 4 | 1 | C320 | 4.7uF Capacitor |
| 5 | 4 | C300, C311, C312, C313 | 10uF Capacitor |
| 6 | 1 | C320 | 47uF Capacitor |
| 7 | 2 | D301, D302 | BAW56 Common Anode Double Diode |
| 8 | 2 | D303, D304 | BAV70 Common Cathode Double Diode |
| 9 | 4 | D305, D306, D307, D309 | B0520LW Schottky Rectifier |
| 10 | 2 | JP301, JP302 | 2-pin Header |
| 11 | 3 | J301, J302, J303 | HDMI Receptacle Connector |
| 12 | 1 | J304 | HDMI Plug Connector |
| 13 | 1 | J306 | Mini USB Female Connector |
| 14 | 2 | Q301, Q303 | MMBT3906 PNP Transistor |
| 15 | 4 | Q302, Q304, Q305, Q306 | MMBT3904 NPN Transistor |
| 16 | 3 | R301, R304, R307 | 1kΩ Resistor |
| 17 | 19 | R302, R303, R305, R306, R308, R309, R311, R330, R332, R333, R335, R338, R340, R341, R343, R346, R348, R349, R351 | 47kΩ Resistor |
| 18 | 2 | R310, R319 | 10kΩ Resistor |
| 19 | 1 | R313 | 0Ω Resistor |
| 20 | 3 | R314, R315, R316 | 2.7kΩ Resistor |
| 21 | 1 | R317 | 68kΩ Resistor |
| 22 | 11 | R318, R320, R322, R323, R324, R325, R326, R327, R352, R353, R354 | 20kΩ Resistor |
| 23 | 1 | R321 | 100kΩ Resistor |
| 24 | 1 | R355 | 2kΩ Resistor |
| 25 | 3 | R356, R358, R360 | 1.5kΩ Resistor |
| 26 | 3 | R357, R359, R361 | 22kΩ Resistor |
| 27 | 12 | R328, R329, R331, R334, R336, R337, R339, R342, R344, R345, R347, R350 | NOT CONNECTED |
| 28 | 1 | SW301 | DIP-8 Switch |
| 29 | 1 | SW302 | DP3T Switch |
| 30 | 1 | U301 | PI3HDMI301 HDMI Switch |
| 31 | 1 | U302 | 1117 Regulator |
| 32 | 2 | U303, U304, U305 | AT24C02B EEPROM |

# Text boxes

HDMI Input Connectors

J301

J303

8-pin Switch

PI3HDMI301

DP3T Switch

J304

HDMI Output Connector

U304

U303

EEPROM (Optional)

3.3V

Regulator

J306

Mini USB Connector

SW302

2”

4”

6”

Input Port 2

Input Port 3

U302

SW301

U305

2”

J302

Input Port 1