PI3HDMI336

PI3HDMI336 HDMI Application Information

Mar. 06, 2011

Contents

- Introduction

- Typical Application

- Application Description

- Layout Design Guide

- Appendix: Typical Application Circuit

# Introduction

PI3HMDI336 is a 3:1 active HMDI switch with I2C configurable interface. Through I2C interface, system designer can easily program and adjust equalization, emphasis, and output swing settings.

With integrated DDC channel MUX, Hot Plug Detection De-Mux, cable plug-unplug detection and HMDI1.4 ARC transmitter, PI3HDMI336 saves GPIO control pins and reduces BOM cost.

Programmable TMDS input termination settings helps designers to avoid the compatibility issue caused by non-standard HMDI source. Programmable output termination setting supports double termination option between PI3HDMI336 and the HDMI receiver chip. This feature minimizes the reflection caused by improper impedance matching and reduces the signal jitter.

# Typical Application

- HPD Output Buffer Mode

Figure 1: Application Diagram of HPD Buffer Mode Provided Scalar DDC 5V Tolerance

In this application, Byte0[3] should be set to 1 through I2C control, external buffer transistor is required on HPDx to avoid 5V to 3.3V leakage. 5V_PORTA, 5V_PORTB and 5V_PORTC are connected to 5V source power for plug or unplug detection. EDID are connected in front of SCLx/SDAx.

- HPD Output Open Drain Mode

Figure 2: Application Diagram of HPD Open Drain Mode Provided Scalar DDC 5V Tolerance

In this application, Byte0[3] should be set to 0 through I2C control, HPDx is pulled up by +5V source power through 1kΩ resistor. 5V_PORTA, 5V_PORTB and 5V_PORTC are connected to 5V source power for plug or unplug detection. EDID are connected in front of SCLx/SDAx.

# Application Description

This part is to describe hardware configuration and I2C control configuration.

- Power Supply

Decoupling capacitors with 10nf value are required to add to each Vcc power pin. Besides, one capacitor with capacitance in the range of 1uF to 10uF is suggested to be incorporated in the power supply bypassing design.

- Address Setting

Pin I2C_ADR is LSB of I2C address. It is pulled down through 100kΩ internally. If I2C_ADR is float or pulled down externally, device address is 0xA8. If I2C_ADR is pulled up externally, device address is 0xA0.

- Plug or Unplug Detection

PI3HMDI336 uses +5V source power to detect if a power-on source is plugged into one of the ports. 5V_PORTA, 5V_PORTB, and 5V_PORTC are connected to +5V source power directly. Plug or unplug status at each port can be also accessible through Byte1 bit[4:2] of I2C control. This is useful for MPU to monitor source plug or unplug at each port.

| Byte Name | Bit | Value | Setting |
| --- | --- | --- | --- |
| Byte 1 | Bit4 | 0 | +5V power of port C is disconnected. |
|  |  | 1 | +5V power of port C is connected. |
|  | Bit3 | 0 | +5V power of port B is disconnected. |
|  |  | 1 | +5V power of port B is connected. |
|  | Bit2 | 0 | +5V power of port A is disconnected. |
|  |  | 1 | +5V power of port A is connected. |

- Interrupt

Pin INT_OUT is output status of INT flag and is an open drain output. So INT_OUT is set to high by external pull up to Vdd through resistor, e.g. 1kΩ resistor.

- ACR Function

PI3HMDI336 only supports ARC single mode input. At ARC input and output, 1uf capacitors are required to add. Besides, one ferrite is suggested to add on ARC output to eliminate noise.

- Equalization

EQ can be adjusted through Byte2 bit[1:0] to meet short cable and long cable. For general sink application, EQ is suggested to choose 12dB as 12dB EQ setting can cover short and long cable, and be used to pass jitter tolerance test.

| Data Byte | Bit 1 | Bit0 | Setting |
| --- | --- | --- | --- |
| Byte 2 | 0 | 0 | 3dB |
|  | 0 | 1 | 6dB |
|  | 1 | 0 | 12dB |
|  | 1 | 1 | 16dB |

- Squelch Control

TMDS output incorporates squelch circuits. To eliminate output oscillation, it is recommended to enable output squelch.

| Data Byte | Bit 4 | Setting |
| --- | --- | --- |
| Byte 2 | 0 | Disable output squelch |
|  | 1 | Enable output squelch |

- Pre-emphasis

Pre-emphasis can be adjusted through Byte2 bit[3:2]. For general sink application, pre-emphasis is suggested to use 0dB.

| Data Byte | Bit 3 | Bit2 | Setting |
| --- | --- | --- | --- |
| Byte 2 | 0 | 0 | 0dB |
|  | 0 | 1 | 1.5dB |
|  | 1 | 0 | 2.5dB |
|  | 1 | 1 | 3.5dB |

- Vswing & Output Mode Settings

TMDS output stage can be set open drain or CML by Byte2 bit[5]. To reduce reflection due to non-ideal input termination in Scalar, CML mode can be selected. For CML output stage, AC swing can be adjusted through Byte2 bit[7:6]. For open drain output, Vswing is only 500mV. In general sink application under CML, AC swing is suggested to use 500mV.

| Data Byte | Output Mode | Bit 7 | Bit6 | Setting |
| --- | --- | --- | --- | --- |
| Byte 2 | CML Bit[5]=1 | 0 | 0 | 500mV |
|  |  | 0 | 1 | 425mV |
|  |  | 1 | 0 | 575mV |
|  |  | 1 | 1 | 500mV |
|  | open drain Bit[5]=0 | X(1) | X | 500mV |

Remark: (1)  X is ‘don’t care’

- HPD Setting

HPD input can be selected to follow HPD_sink or I2C register Byte0 bit[2:0].

| Byte Name | Bit 4 | Setting |
| --- | --- | --- |
| Byte 0 | 0 | HPD_SINK |
|  | 1 | Byte0 bit[2:0] |

Provided that HPD input selection in Byte0 bit4 is set to use Byte0 bit[2:0], HPD input C/B/A can be controlled by Byte0 bit[2:0] and Byte0 bit[3].

| Byte Name | HDP Mode | Bit 2/1/0 | Setting |
| --- | --- | --- | --- |
| Byte 0 | open drain bit[3] = 0 | 0 | HPD C/B/A = low |
|  |  | 1 | HPD C/B/A = high |
|  | buffer bit[3] = 1 | 0 | HPD C/B/A = high |
|  |  | 1 | HPD C/B/A = low |

- Standby Control

TMDS output channels can be enabled or disabled by Pin /OE or I2C Byte0 bit[5]. When Byte0 bit[5] is set to 0, HDMI336 enters into standby mode and TMDS output is disabled to save power.

| Byte Name | Bit 5 | Setting |
| --- | --- | --- |
| Byte 0 |  |  |
|  | 0 | Disable TMDS output |
|  | 1 | Enable TMDS output |

- Port Selection

Byte0 bit[7:6] are used to select the connections of which TMDS input port to TMDS output port and which SCL and SDA port to SCL_SINK and SDA_SINK.

| Byte Name | Bit 7 | Bit 6 | TMDS Output Port | SCL_SINK / SDA_SINK |
| --- | --- | --- | --- | --- |
| Byte 0 |  |  |  |  |
|  | 0 | 0 | TMDS Input Port 1 | SCL_A / SDA_A |
|  | 0 | 1 | TMDS Input Port 2 | SCL_B / SDA_B |
|  | 1 | 0 | TMDS Input Port 3 | SCL_C / SDA_C |

- DDC Mode Selection

DDC channel offers a selection of passive switch and active switch buffer. To minimize the DDC capacitance, active switch buffer is recommended for long trace application.

| Data Byte | Bit 0 | Setting |
| --- | --- | --- |
| Byte 1 | 0 | Passive Switch |
|  | 1 | Active Switch Buffer |

- Input Termination

As PI3HMDI336 has built-in input termination at TMDS differential input, there is no need to add external termination resistor. TMDS input can be configured to pull up to +3.3V through Rt(50Ω) which is an input termination, or pull down to GND through Rd(200k) and TMDS input is Hi-z to eliminate input noise interference .

| Byte Name | Bit7/6/5 | Setting |
| --- | --- | --- |
| Byte 1 | 0 | Rt(50Ω input termination) is connected; Rd(200k)is disconnected. |
|  | 1 | Rt(50Ω input termination) is disconnected; Rd(200k) is connected. |

# Layout Guide Line

Figure 3: Demo Board PCB 2-Layer Layout

- TMDS lines

- Proper stack up data is selected for 100Ω differential impedance control for high speed TMDS lines. Please refer to figure 4.

- If vias or passive components are unavoidable, spacing between the differential pair should be widened before them and they should be placed symmetrically as shown in figure 5.

Figure 4: Stack up of TMDS line

Figure 5: Layout of Vias and Passive Components on Differential Trace

- Power/Ground

Traces for power and ground should be wide and short.

- ARC Impedance Control

ARC impedance is well controlled to 55Ω.

- Decoupling Capacitors

Decoupling capacitors should be close to each Vcc pin. As PI3HMDI336 has 6 Vcc pins including one SVDD pin, 6 de-coupling capacitors with 0.1uF are needed. In figure 6, C201-C206 are decoupling capacitors.

Figure 6: Layout of Decoupling Capacitors

# Appendix: Typical Application Circuit

Figure 7: Application Circuit of HPD Buffer Mode Provided Scalar DDC 5V Tolerance

Figure 8: Application Circuit of HPD Open Drain Mode Provided Scalar DDC 5V Tolerance