PI5USB1468 / PI5USB1468A

PI5USB1468/PI5USB1468A EVB Rev.A User Manual

by Noyes Mok

Introduction

Pericom’s PI5USB1468 and PI5USB1468A are the USB sleep & charge switch with Vbus switch control function which provides multimode supports auto-detection and auto-switching between modes by detecting correctly plugged in device.

The PI5USB1468 series evaluation board (EVB) is designed to demonstrate the benefits, performance and key features of PI5USB1468 and PI5USB1468A. This user manual describes the usage of this EVB and it will be divided into following sections:

- Overview

- Quick start

- Board Design information

    - PI5USB1468/PI5USB1468A EVB Schematic

    - PCB Layout

    - PCB Layout Reference

    - BOM List

Overview

Figure 1(a) & 1(b) are the block diagrams of Pericom PI5USB1468/PI5USB1468A Evaluation board (EVB) and Figures 2(a) & (b) are the top and bottom view of EVB board. There is an USB plug connectors (J2) which is used to connect PC’s USB port and the USB receptacle connector (J1) is used to connect mobile devices.

An external Vbus switch PI5PD2068/PI5PD2069 is assembled on EVB which is controlled by the INT# / INT pin of PI5USB1468/PI5USB1468A.

The MODE setting in SW1 is used to select the normal USB operation and simulate the Standby or Sleep mode (S3/ S4) of the PC. The LED D1 is used to show whether the circuit is over-current or over-temperature. PI5USB1468/PI5USB1468A operation required +5V which was supplied by the PC through the USB connector (J2) or external power supply +5V through JP2 & JP3.

Figure 1a, block diagram of PI5USB1468 EVB

Figure 1b, block diagram of PI5USB1468A EVB

Figure 2(a), top view of PI5USB1468/PI5USB1468A EVB        Figure 2(b), bottom view of PI5USB1468/PI5USB1468A EVB

Quick Start

To start-up the PI5USB1468/ PI5USB1468A EVB, complete the following steps:

- Check the head pin status and SW1 setting follow Table 1

- EVB USB connector J2 plugged into PC’s USB connector.

- For Normal USB operation, SW1 switch to RIGHT side (SB# = 1 - Normal USB mode)

For Auto sleep and charge mode on mobile device charging, SW1 switch to LEFT side (SB# = 0 - Auto sleep and charge mode)

- Power up the PC

- Plug the mobile device into EVB USB connector J1

Header pin is set as defaulted on EVB.

| Header pin # | Pin name for PI5USB1468 | Pin name for PI5USB1468A | Switch status | Remark |
| --- | --- | --- | --- | --- |
| JP1 | VBUS_OUT | VBUS_OUT | Short |  |
| JP4 | VDD | VDD | Short | EVB power up by the PC |
| JP5 | SEL | SEL | Short | SEL = H |
| SW1 | Configure mode | Configure mode | LEFT → SB#=0 (Auto sleep and charge) RIGHT → SB#=1 (Normal USB mode) |  |

- Auto sleep and charge mode was set as default on EVB

Table 1, Header pin settings for EVB (header pins location refers to Figure 4)

Figure 3, Connection of PI5USB1468 / PI5USB1468A EVB

Detail Description

The functionality of header pins, switch are detail described in this section.

Functionality of Header Pins & Banana Jack

| Header Pin | Description | Remark |
| --- | --- | --- |
|  | PI5USB1468 | PI5USB1468A |  |
| JP1 | Pin 1 = PI5PD2068 output Pin 2 = Vbus pin of USB receptacle connector | Pin 1 = PI5PD2069 output Pin 2 = Vbus pin of USB receptacle connector | Short = connect the +5V output to USB receptacle connector |
| JP4 | Pin 1 = Vbus from USB plug Pin 2 = VDD of PI5USB1468 | Pin 1 = Vbus from USB plug Pin 2 = VDD of PI5USB1468A | Short = EVB power up by Vbus of USB plug Open = EVB need to power up by external power supply |
| JP5 | Pin 1 = 10kohm to +5V Pin 2 = SEL of PI5USB1468 | Pin 1 = 10kohm to +5V Pin 2 = SEL of PI5USB1468A | Short → SEL = high Open → SEL = Low |
| Banana Jack | PI5USB1468 | PI5USB1468A | Remark |
| JP2 | GND | GND | If use external power support, JP4 must be Open |
| JP3 | +5V from external power support | +5V from external power support |  |

Functionality of Switches

| Switch | Pin on PI5USB1468/ PI5USB1468A | Description |
| --- | --- | --- |
| SW1 | SB# | Configure Mode, 0 (LEFT side) = Sleep and charge mode, 1 (RIGHT side) = Normal USB mode |

Switches and header pin Setting

| SB# | SEL | Feature |
| --- | --- | --- |
| SW1 | JP5 |  |
| 0 | 0 | Auto Sleep & Charge - with keyboard/mouse pass through |
|  | 1 |  |
| 1 | 0 | S0 charging with SDP only |
|  | 1 | S0 charging with CDP / SDP (depends on external device) |

Board Design Information:

  - PI5USB1468/PI5USB1468A EVB Schematic

Remark: The EVB layout for PI5USB1458, PI5USB1458A, PI5USB1468 and PI5USB1468A are the same.

- PCB Layout

Figure 4, Top view of PI5USB1468/PI5USB1468A EVB Layout

Figure 5, Bottom view of PI5USB1468/PI5USB1468A EVB Layout

- PCB Layout Requirements

- Stack Up:

| Layer # | Plane | Material Type | Thickness (mil) |
| --- | --- | --- | --- |
|  | Solder Mask |  | 0.4 |
| Layer 1 | Signal |  | 1.2 |
|  | Prepreg | FR4 1080 FR4 2216 | 7.3 |
| Layer 2 | GND |  | 1.2 |
|  | Core |  | 44 |
| Layer 3 | Power |  | 1.2 |
|  | Prepreg | FR4 2216 FR4 1080 | 7.3 |
| Layer 4 | Signal |  | 1.2 |
|  | Solder Mask |  | 0.4 |

- Isolation Spacing = 30 mil

- Width & Spacing (W/S) of 90Ω Differential Trace = 11 / 10 / 11 mil

- BOM List

| Item | Quantity | Reference | Description |
| --- | --- | --- | --- |
| 1 | 1 | C1 | 4.7uF Capacitor |
| 2 | 3 | C2, C3, C5 | 0.1uF Capacitor |
| 3 | 1 | C4 | 22uF Capacitor |
| 4 | 1 | D1 | Red LED |
| 5 | 3 | JP1, JP4, JP5 | 2X1 Header Pin |
| 6 | 2 | JP2, JP3 | Banana Jack |
| 7 | 1 | J1 | USB 2.0 Receptacle connector |
| 8 | 1 | J2 | USB 2.0 Plug connector |
| 9 | 1 | R1 | 560Ω Resistor |
| 10 | 6 | R2, R3, R4, R5, R6, R14 | 10kΩ Resistor |
| 11 | 1 | SW1 | SPDT switch |
| 12 | 1 | U1 | PI5PD2068 / PI5PD2069 |
| 13 | 1 | U2 | PI5USB1468 / PI5USB1468A |

# Text boxes

J1

INT

J1 USB Receptacle

INT#

D1

SW1

SB#

EN

PI5PD2069

SW1

Switch for Mode select

2

1

PI5USB1468

VBUS_IN

JP4

J11

JP1

USB Plug

PI5USB1468A

J2

USB Plug

J1 USB Receptacle

EVB plug-into PC USB port

Mobile device

J2

PI5USB1458/PI5USB1458A EVB

PC

USB Receptacle

OUTPUT

JP5

INPUT

For PI5USB1468A, put 10k on R2 and R3 floating

J2

USB Plug

SW1

J2

Normal USB mode

Auto

Sleep & Charge

D1

EN#

2

1

PI5PD2068

Switch for Mode select

SB#

INPUT

USB Plug

USB Receptacle

OUTPUT

For PI5USB1468, put 10k on R3 and R2 floating

LEFT side = Sleep and charge mode

RIGHT side = USB mode

GND

GND

VBUS_IN